## Slide 1: Sign Design Simplified
Mastering ADA and Signage Regulations
By Steve Harroun

## Slide 2: WHO AM I?
  Owner of Harroun Designs Inc.
  Based in Pittsburgh, PA
  20 years in the sign industry
  ISA Board of Directors
  Pleasant Hills Planning Commissioner
  Candidate for PH Borough Council
  US Coast Guard veteran and TOTAL sign geek!
Let’s connect on LinkedIn!

## Slide 3: WHO ARE YOU?
  National / Large Sign Company
  Medium or Small Sign Company
  Sign / Graphic Designer
  Owner
  End User
  Installer
  Auditor

## Slide 4: OUR GOAL TODAY
    Empower you with the knowledge and tools to identify non-compliant signs
    The ability to design ADA & code compliant signs
    Increase sales

## Slide 5: WHAT’S THE DIFFERENCE?
  Codes: IBC, NFPA, NRC, DHS, etc.
    First developed to prevent fires
    Help to ensure safety, health, and general welfare of occupants
    Applies to new construction and major renovations
    Enforced by local and state governments
  ADA
    First developed in 1980’s.
    Prohibit discrimination based on disabilities in areas of public life
    Provide accessibility to ensure equal access to buildings, services, and programs
    Applies to facilities covered by the ADA, including new construction, renovations, and existing buildings
    Enforced by the DOJ (Federal law) and tried in Federal or civil courts
    Includes TACTILE and VISUAL signs

## Slide 6: Timeline of Codes and Laws
1600’s
1800’s
1915
1918
1927
1990
1994
2000
2010
2025
Boston created codes to prevent fires
More comprehensive codes established nation-wide
Building Officials & Codes Administration (BOCA) established
Codes grouped under ANSI
Unified Building Code published
(UBC)
ADA becomes Federal Law
BOCA & UBC consolidated into ICC
First set of ICC codes published
First update to ADA 3/15/10
1960
ANSI Publishes the A117.1 Barrier Free Standard
1968
Architectural Barriers Act becomes law

## Slide 7: WHEN DO YOU NEED TACTILE SIGNS?
  Tactile ADA signs are required to identify permanent spaces for those with visual impairments.
  Examples:
  Restrooms, Locker Rooms, Mechanical, Electrical, Cafeterias, Libraries
  Room Numbers
  Floor Levels
  Exit doors, Exit stairs, Exit passageways, and Exit Discharge
  Areas of Refuge (Rescue Assistance)

## Slide 11: EXEMPTIONS
The following signs are exempt from ADA

## Slide 12: Logos

## Slide 13: Building Addresses

## Slide 14: Occupant Names and Titles

## Slide 15: Menus

## Slide 16: Seat and Row Designations

## Slide 17: Parking Facilities, Except Exit Routes

## Slide 18: Temporary Signs In Place for Less Than 7 Days

## Slide 19: Signs in Non-Public Spaces in Correctional Facilities

## Slide 20: RULES FOR TACTILE SIGNS
    Permanent room ID name in tactile copy w/ Grade 2 braille
    Copy and braille raised 1/32” above the face of the sign
    Minimum and maximum character height 5/8” – 2”
    Letters must be ALL UPPERCASE
    Only thin stroke fonts – width of uppercase “O” is 55% min & 110% max height of an “I”
    Only sans serif fonts - no decorative or scripted fonts (NEVER Comic Sans)
    Required a minimum of 1/8” between characters (kerning)
    Line spacing: Minimum 135%, Maximum 170% height of capital letter “I”
    Symbols must be ABOVE tactile characters
      Symbols must be in a 6” clear vertical field
      Symbols are NOT required to be raised
    New rules for 2025 Characters must contrast w/ the background
      New minimum LRV contrast of 65% required
      Must be able to be verified by the manufacturer, testing labs, or field measured

## Slide 21
LRV B1
100
LRV B2
10.83
MECHANICAL
MECHANICAL
[(100-10.83)] / 100 x 100 = 89.17
[(B1-B2) / B1 X 100 = Contrast
B1 Lighter Color
B2 Darker Color

## Slide 22: HOW DO VISUALLY IMPAIRED FIND SIGNS?
    Mount signs in a consistent location next to the door and mount signs at a consistent height

## Slide 23: MOUNTING LOCATIONS
    Latch side of the door
    Nearest adjacent wall
    If the door opens towards you, the COPY must be centered 9” from the door, “centered in an 18” clear floor space of the swing of the door”
    You CAN mount to doors if you meet 3 criteria (think of hotels)
      Door opens away from you
      There are NO hold-open devices
      The door has automatic closures
    If there are double doors and one is typically locked, mount on the locked door
    If both double doors open towards you, copy must be centered 9” from the open door
    If there are sidelights, mount on the glass
      I recommend vinyl on the front of the glass, then mount on the vinyl
    Baseline of the TACTILE COPY minimum 48” maximum 60” AFF

## Slide 24: Consistent Height, Latch Side of the Door

## Slide 25: Nearest Adjacent Wall

## Slide 26: Locked Wing Door

## Slide 27: Outside Swing of Doors

## Slide 28: On Glass if There Are Side Lights

## Slide 30: RULES FOR VISUAL SIGNS
    Upper & Lower case allowed
    Serif fonts permitted
    Italic, decorative or unusual fonts are NOT allowed – Still NO Comic Sans
    Character proportions have the same requirements as tactile signs
    You are allowed a wider variety of stroke thickness
    Character spacing has a range: Minimum 10%, Maximum 30% of the copy height
    Line spacing requirements are the same as tactile copy
    New rules for 2025 Characters must contrast w/ the background
      New minimum LRV contrast of 65% required
      Must be able to be verified by the manufacturer, testing labs, or field measured
    Copy height requirements are determined by height of sign & distance from the viewer

## Slide 31
    48”
    70”
    6’
    5/8” MIN Copy Height

## Slide 32
    70”
    120”
    15’
    2” MIN Copy Height

## Slide 33
    ABOVE 120”
    21’
    3” MIN Copy Height

## Slide 34: AREAS OF REFUGE
    Doors leading to Areas of Refuge should be identified with a sign that has the International Symbol of Accessibility and tactile copy “AREA OF REFUGE”
    If the Area of Refuge has a 2-way communication system, you must post instructions on how to use the communication system, directions to other means of egress, instruct people to exit, unless they are assisting others, planned availability of assistance, and how to summon assistance for assisted use of elevators, if available.

## Slide 35: STAIR SIGNS

## Slide 36: STAIR SIGNS: UP TO 4 FLOORS
    Buildings up to 4 floors
      Stair ID ADA sign outside stairwell
      Floor ID ADA sign inside stairwell

## Slide 37: STAIR SIGNS: 4 FLOORS +
    Buildings 4 floors and up
      Stair ID ADA sign outside stairwell
      Floor ID ADA sign inside stairwell
      Stair informational sign inside stairwell (NOT TACTILE)

## Slide 38: STAIR SIGNS: 4 FLOORS + 75 FEET +
    Buildings 75’ and taller, “high rise”
      Stair ID ADA sign outside stairwell
      Floor ID ADA sign inside stairwell - Photoluminescent
      Stair informational sign inside stairwell (NOT TACTILE) - Photoluminescent

## Slide 39: POP QUIZ!
We will review some signs in the real world.
Put in the chat if you can tell us if they are compliant, non-compliant, mounted incorrectly,
or exempt!

## Slide 40
✅
🚫

## Slide 41
    703.2.6 Stroke Thickness
    Stroke thickness of the uppercase “I” shall be 15% max of the height of the character.
    ***University of Pittsburgh case study***

## Slide 42
🚫

## Slide 43
    703.2.7 Character Spacing
    Spacing between the baseline of separate lines of tactile copy within a message shall be 135% min to 170% max of the raised character height.
    703.4.2 Location
    Where a tactile sign is provided at a door, the sign shall be located alongside the door at the latch side. Signs with tactile characters shall be permitted on the push side of doors with closers and without hold-open devices.

## Slide 44
✅

## Slide 46
🚫

## Slide 47
    703.4.1 Height Above Finish Floor or Ground
    Tactile characters on signs shall be located 48” min AFF, measured from the baseline of the lowest tactile character and 60” AFF, measured from the baseline of the highest tactile character.

## Slide 48
🚫

## Slide 49
    703.2.2 Case
    Characters shall be uppercase.
    703.6.1 Pictogram Field
    Pictograms shall have a field height of 6 inches min. Characters and braille shall not be located in the Pictogram field.
    703.6.3 Text Descriptors
    Pictograms shall have text descriptors located directly below the pictogram field. Text descriptors shall comply w/ 703.2, 703.3, and 703.4.

## Slide 50
🚫

## Slide 52
    Now it’s your turn!

## Slide 53
🚫

## Slide 54
🚫

## Slide 55
🚫

## Slide 56
✅

## Slide 57
🚫

## Slide 58
✅

## Slide 59
🚫

## Slide 60
🚫

## Slide 61
🚫

## Slide 62
🚫

## Slide 63
🚫

## Slide 64
✅

## Slide 65
🚫

## Slide 66
🚫

## Slide 67
🚫

## Slide 68
🚫

## Slide 69
✅

## Slide 70
🚫

## Slide 71
🚫

## Slide 73
🚫

## Slide 74
🚫

## Slide 75
🚫

## Slide 76
🚫

## Slide 77
🚫

## Slide 78
✅
🚫

## Slide 79
🚫

## Slide 80
✅

## Slide 81
✅
🚫

## Slide 82
🚫

## Slide 83
🚫

## Slide 84
✅

## Slide 85
    One More!

## Slide 86
✅
🚫

## Slide 87: USE THIS INFORMATION FOR SALES
Identify non-compliant signs in the field
Provide solutions for your clients
Design compliant signage
Prove competence and expertise to your clients
If you see non-compliant signs, provide a solution
Increase your standard offerings to include ADA and code signage
💰
💵
🤑

## Slide 88
Thank You!
Please let me know if you have any questions or comments!